## Slide 1
Acts, Management Strategies and Techniques of Soil Erosion and Conservation in Taiwan
Department of Soil and Water Conservation
National Pingtung University of Science and Technology
Shih-Hao Jien
Notes: Hello, everyone. I am Kun-Ting CHEN, Assistant Professor, form Department of Civil Engineering, NPUST.
Today, I would like to introduce Landslide Dam Formation.

## Slide 2
2
Soil and Water Conservation Acts in Taiwan
Topsoil erosion in Taiwan
Conservation techniques and case studies
Taiwan’s current issues in soil and water conservation
Contents（Part I ）

## Slide 3: Geologic characteristics of Taiwan
2022/9/1
The geographic distribution and the tectonic
setting of Taiwan.
(modified from Angelier, 1986)
Total area: ~36,000 km2
Slopeland area (≥ 100 m): ~74%
Maximum elevation: 3,952 m
Average elevation of slopelands: 660 m
Average slope gradient of slopelands: 25 degree

## Slide 4: Rainfall amounts and Renewable internal freshwater resources capita
2022/9/1
Renewable internal freshwater resources capita (m3/person/year)
Annual rainfall (mm/year)
2.6
times
World average
Taiwan

## Slide 5
2022/9/1
>5950.5 mm
6643.5 mm
>5540 mm
2019 annual rainfall amounts

## Slide 6: Sedimentation of major reservoirs in Taiwan
Reservoir sedimentation (%)
> 30%
Northern
Taiwan
Southern Taiwan

## Slide 7: Multi-disasters in Taiwan
Soil erosion
Landslides
Debris flow
Rock falls
Disaster Prevention Technology Research Center, Sinotech Engineering Consultant, Inc. http://dptrc.sinotech.org.tw

## Slide 8: The Acts regarding soil and water conservation
Slopeland Conservation and Utilization Act (from 1976)
Enforcement Rules of Slopeland Conservation and Utilization Act
Soil and Water Conservation Act (from 1994)
Enforcement Rules of Soil and water Conservation Act
Soil and Water Conservation Handbook (2019)
  http://law.coa.gov.tw/GLRSnewsout/EngLawQuery.aspx
2.
https://www.swcb.gov.tw/Home/Download/download_more?id=e360809476ae4 80996c68666f39102d2
You could download the Acts from here
8

## Slide 9: Soil erosion in Taiwan
9
Most of soil erosion in Taiwan are resulted from unsuitable agricultural behaviors and overuse of slopelands.
We have established basic databases for calculating soil erosion potential, such as soil types; soil erodibility factor (K factor) and soil erosivity (R factor) from1976.
🞑 Soil survey in slopelands (1976-1987);
🞑 Distribution of K factor (Wann and Huang,1989);
🞑 Distribution of R factor (Huang et al.,1979; Lu et al., 2005);
🞑 Distribution of soil erosion potential at some important watersheds in Taiwan (Chen et al., 2009; Lin et al., 2012).

## Slide 10: History of Soil Survey in Taiwan
10
Soil survey in Taiwan has been conducted by Japanese soil
scientists for making the soil maps of pH and texture since 1920s.
20 survey projects were conducted as the important events in the past 50 years since 1950s.
Some of significant contributions in providing very valuable information on human life, such as agricultural development, designing agricultural policy with ecological and environmental concern, and soil education.

## Slide 11
11
1991
2008
2018

## Slide 12: 1. Important survey projects in the last 50 years in Taiwan (1946-2016)
1. Reconnaissance soil survey of Taiwan (1946-1952) － Taiwan Agricultural Research Institute (TARI), Council of Agriculture
2. Soil survey and soil fertility evaluation － Taiwan
Fertilizer Company (TFC)
3. Soil Survey of Taoyuan county － TFC
4. Soil survey of Tobacco production of Taiwan － Department of Agricultural Chemistry, College of Taiwan Provincial Agriculture

## Slide 13: Important survey projects in the last 50 years in Taiwan (continued)
5. Soil survey of agricultural farms － Taiwan Sugar Company (TSC)
6. Soil survey for land use of agriculture and forestry － TARI
7. Soil survey of Tea production in Kuang-See township － Department of Agricultural Chemistry, National Taiwan University (DAC/NTU)
8. Detail survey of Taiwan saline soils － DAC/NTU
9. Soil survey and land use of Lu-Kang region of Changhwa
county － TFC

## Slide 14: Important survey projects in the last 50 years in Taiwan (continued)
10. Soil survey of saline soil along seashore － TSC
11. Detailed soil survey of Taiwan rural soils － National Chung Hsing University (NCHU) (1962-1976) and TARI (1974-1979)
12. Soil survey of Southern region of Taipei Basin － TFC
13. Reconnaissance soil survey of Taiwan Forest soil －
Forestry Bureau of Taiwan Province

## Slide 15: Important survey projects in the last 50 years in Taiwan (continued)
14. Detailed soil survey of Taiwan hill land (1980-1988) －
Bureau of Agriculture and Livestock of Hill Land, Taiwan Province
15. Survey of contaminated soils (1984-2000) － NCHU, NTU, Agricultural Chemical and Toxic Materials Research Institute (TACTRI), and National Pingtung University of Science and Technology (NPUST)
16. Survey of soil productivity grade of upland in Taiwan (1986- 1990) － Department of Soil Science, NCHU (DSS/NCHU)

## Slide 16: Important survey projects in the last 50 years in Taiwan (continued)
17. Detailed soil survey of Taiwan forest soils, which the elevation ranged from 1000m to 4000m (1993-2002) － TFRI
18. Detailed grid soil survey of Taiwan rural soils (2000-2010)
－ TARI
19. Soil quality monitoring project after different soil management system (1997-2007) － TARI
20. Project of soil resource information establishment in Taiwan
(the 1st stage) (2008-2016) － TARI

## Slide 17: 8 most important soil survey projects of 19 items

## Slide 18: Reconnaissance soil survey of Taiwan Province (1946-1952)
8 volumes of soil survey reports were published:
🞑 Taichung, Penghu, Tainan, Kaohsiung, Pingtung, Taoyuan, Hsingchu, and Maoli
🞑 Soil maps on the scale of 1:100,000
Soil mapping unit:
🞑 Soil series, soil types and soil phase
All soil survey followed Soil Taxonomy (1938, USDA)
Soil survey was conducted by TARI

## Slide 19: Detailed soil survey of Taiwan rural soils (1962-1976, 1974-1979)
Soil survey was conducted by DSS/NCHU during 1962-1976
7 volumes of soil survey reports were published
90 soil maps (1:25,000) were published
342 soil series were established
Soil type as mapping unit (soil series + surface texture)
Soil survey was conducted by TARI during 1974-1979
  4 volumes of soil survey reports were published
  88 soil maps (1:25,000) were published
  278 soil series were established
  Soil type as mapping unit

## Slide 20: Detail soil survey of Taiwan hill lands (1980-1988)
13 volumes of soil survey reports of whole Taiwan hill lands
215 soil maps on the scale of 1:25,000
432 soil series were established
Soil phase as mapping unit (soil series + surface texture+ slopes)
Soil survey was conducted by Bureau of Agriculture and livestock of hill land

## Slide 21: Soil survey of productivity grade of Taiwan upland (1986-1990)
4 classes of soil productivities were established, depend on:
🞑 the existence of texture changes of soil profile
🞑 gray mottles formed at different soil depths
168 soil maps of soil productivity classes of Taiwan upland (1:25,000)
were published
Soil survey was conducted by DSS/NCHU

## Slide 22: Soil survey of contaminated soils (1984-2000)
≧10,000 soil sampling locations, 150 potential polluted sites, and 5 seriously polluted sites have been included into this GIS system
Soil survey was conducted by NCHU, NTU, TACTRI and NPUST
Rural soils (1984-1987 )
potential contaminated soils (1988-1994 )
highly potential contaminated soils (1995-2000 )
4 km
4 km
1 km
1 km
100 m
100 m
GIS

## Slide 23: Detailed soil survey of Taiwan forest soils in Mountains (1993-2002)
10 volumes of soil survey reports were published
≧200 soil maps (1:50,000) were published
9 Soil Orders were classified
< 50 soil series were established.
Soil phase as mapping unit.
The major Soil Order distributed in the forest soils
Soil survey was conducted by TFRI
Soil Orders | Area (km2) | % of land use
Inceptisols | 7,415 | 44
Entisols | 5,923 | 35
Alfisols | 1,805 | 11
Ultisols | 1,250 | 7

## Slide 24: Detailed grid soil survey of Taiwan rural soils (2000-2010)
Sample interval
🞑 Every 250 meters based on 1:5,000 air photo pictures
Sampling depth
🞑 0-15cm, 15-30cm, 30-60cm, 60-90cm, 90-120cm, and 120-150cm depth
≧ 130,000 soil profiles (780,000 soil samples) database in whole Taiwan
🞑 Included into the GIS system of National Soil Information System of Taiwan
Soil survey was conducted by TARI

## Slide 25
六甲
官田
東山
柳營
新市
將軍
台南市安南區
白河
後壁
鹽水
新營
北門
學甲
下營
楠西
麻豆
佳里
大內
七股
玉井
善化
西港
山
安定
上
左鎮
新化
永康
台南市西區
台南市東區
圖 例
鉀肥管理
施用鉀肥極有效 一般作物不缺鉀肥
園藝作物不缺鉀肥
鉀肥過量
(郭鴻裕, TARI)

## Slide 26
東山
六甲
後壁
白河
柳營
將軍
台南市安南區
台南市北區
台南市安平區
台南市東區
鹽水
新營
北門
學甲
下營
楠西
麻豆
官田
佳里
大內
七股
善化
西港
山上
安定
新市
左
玉井
南化
鎮
新化
永康
圖 例
磷肥管理
磷肥肥效極大 磷肥肥效中等 磷肥肥效小 無明顯肥效
(郭鴻裕, TARI)

## Slide 27: Soil Quality Monitoring project after different soil management system (1997-2007)
150 rural soil sites were selected
🞑 Including different soils, crops, and climates conditions
🞑 Monitoring the changes of soil quality in each site
Soil quality indicators
🞑 soil texture
🞑 pH
🞑 organic C
🞑 total N
🞑 exchangeable K, Na, Ca, Mg, and Mn (extracted by 0.1M sodium acetate at pH7)
🞑 soluble Fe, Mn, Cu, Zn, Cd, Pb, Cr, and Ni (extracted by 0.1M HCl)
🞑 available P, K, Ca, Mg, Na, B, Cu, Zn, Fe, and Mn (extracted by Mehlich #3
solution)

## Slide 28: Contents（Part II ）
2
Soil and Water Conservation Acts in Taiwan
Topsoil erosion in Taiwan
Conservation techniques and case studies
Taiwan’s current issues in soil and water conservation

## Slide 29: Land uses in sloplands and mountains (Taiwan)
2022/9/1
In Taiwan, 65% of slopelands
are for crop production

## Slide 30: Over-using of slopelands
2022/9/1

## Slide 31: Fruit gardens everywhere at watersheds in Taiwan mountain areas
2022/9/1

## Slide 32: Betel nut planting in Taiwan mountain areas
2022/9/1

## Slide 33: Soil erosion in Taiwan
Soil erosion rate
<5 tons/ha/yr of natural land with good surface cover or
natural forest ecosystem
Serious on some cultivated hill lands (50-100 tons/ha/yr) during the typhoon seasons
The highest soil loss (>200-500 tons/ha/yr) caused by a strong storm owing to climate changes in last decade.
We lack soil erosion map in Taiwan

## Slide 34: Soil loss evaluation in Taiwan
2022/9/1
K factor
(Wann and Huang, 1989)
LS factor
Dynamic
Dynamic
R factor
(Lu et al., 2005 )

## Slide 35: Precipitation in Taiwan
2022/9/1
Annual precipitation: ~2,600 mm, mainly in May to Sept. (~2000 mm)
Rainfall duration decreases & intensity increases
R factors

## Slide 36: Changes of soil erodibility factor (K factor) at a terrace in southern Taiwan (for example in Laopi terrace)
38
1990 2011
0.010 – 0.020
0.015 – 0.075
1.5 – 3.5 times

## Slide 37
39
Land uses migration
1990
2011

## Slide 38: Re-evaluation of K factor for recent landuses
40
2011

## Slide 39: Which land use do result in most serious soil erosion in agricultural slopelands?
41
2022/9/1
Landuses | K factor
Bare lands | 0.022
Banana | 0.021
Lichi fruit | 0.024
Pineapple | 0.018
Bamboo | 0.013
Broadleaf | 0.016

## Slide 40: Soil loss evaluation in Shihmen watershed (northern Taiwan)

## Slide 41: Common techniques for preventing top soil erosion in Taiwan
Agronomic methods:
🞑 Contour planting
🞑 Bench terrace
🞑 Mulching
🞑 Drainage ditch
Engineer methods (usually used for steep slopes : > 40 degree):
🞑 Geotextile mets
🞑 Piling and wattling

## Slide 42
44
2022/9/1
Check dam Slit dam Spur dike
Retention pond Deposit pond Drainage Gauge Retaining wall
Earth-filling dam Dike
Sowing
Direct sowing Spray planting Vegetation bags Soil bags
Tree planting Grass planting
Vegetation methods
Engineering methods
Agronomic
methods
Contour planting Bench terrace Mulching Drainage ditch

## Slide 43
2022/9/1
45

## Slide 44
Contour planting
Bench terrace

## Slide 45
2022/9/1
Excavation part
Filling part

## Slide 46
2022/9/1

## Slide 47: Case study in reducing soil erosion in Lichi garden by different agronomic methods (Chiang, 2005)
2022/9/1
 | Treatments | techniques | Soil losses (kg) | Runoff contents (m3) | 
 | A | Cover with grass | 75.6 | 46.7 | 
 | B | Cover with grass; drainage ditch | 2.13 | 11.9 | 
 | C | Without cover and mulching | 2820 | 86.9 | 
 | D | Mulching with grass residuals | 123 | 48.9 | 
Slope gradient: 31°(60%); Slope length: 22.13 m; Width: 4 m

## Slide 48: Engineering methods:
Covered by rolled erosion control products (RECPs) and Spray seeding
Piling and watting

## Slide 49
2022/9/1

## Slide 50: Case study in reducing soil erosion at watersheds in Shihmen reservoir by different engineering methods (Lin et al., 2013) 2008.09 – 2010.12
2022/9/1
Nail block = 55
treated
natural
Bare slopes
Eroded soil depth (mm)
Rainfall amounts (mm)
treated
mulch
RECPs
Piling &
wattling
Percentage of erosion reduced (%)

## Slide 51: Strategies of preventing top soil erosion
Establishment of regulations in using limitation of slopelands.
Development and selection of suitable agronomic and engineering techniques for soil loss reducing, particularly in high soil erosion areas.

## Slide 52: Criterion of slopeland using limitation in Taiwan
Degree | Slope gradients | 
S1 | < 5% | Degree Soil depth (cm) D1 > 90 D2 51 - 90 D3 20 -50 D4 < 20
S2 | 5% - 15% | 
S3 | 16% - 30% | 
S4 | 31% - 40% | 
S5 | 41% - 55% | 
S6 | > 55% | 
2022/9/1
Criteria | Degree |  | properties | 
Agricultural uses | I |  | (S1, D1); (S1, D2) | 
 | II |  | (S1, S2, D1); (S2, D2); (S1, D3) | 
 | III |  | (S4, D1); (S3, D2); (S2, D3) | 
 | IV | 1 | (S5, D1); (S5-S4, D2); (S4-3, D3); (S1-3; D4) | 
 |  | 2 | (S5, D3); (S4, D4) | Without disturbance
Forest only | V |  | (S6, D1-3); (S5-6, D4); (S5, D3); (S4, D4) | 
Conserved | VI |  | Severe soil erosion (gully erosion) | 

## Slide 53: Strategies to prevent soil loss in Taiwan
The best management practices (BMPs) to reduce top soil loss in last 3 decades in Taiwan
Contour Planting & Bench Terrace
55
Grass Cover and Mulching
Piling and Wattling
RECPs using

## Slide 54: Conclusions
Well-establishment of basic database is necessary before soil erosion potential evaluation
  Rainfall data (for R value);
  Soil properties and types (for K value);
  Land uses investigation (for C values).
To focus on areas with high erosion potential and select suitable conserved techniques and BMPs to minimize impaction on soils and environment:
  Agronomic techniques: < 40degree of slope gradient
  Engineering techniques: ≥ 40 degree of slope gradient

## Slide 55
Soil and Water Conservation
Thank You