## Slide 1
Basic Hydrology
Department of Soil and Water Conservation
National Pingtung University of Science and Technology
Jie-Lun Chiang

## Slide 2
This cycle starts with evaporation (from ocean and land). During known processes in the air, it will change to precipitation and come to land and ocean again. Some part of precipitation will infilter in the soil where can recharge groundwater and extra amount
of water (in saturation layer of soil) change into groundwater flow and finally discharge to the ocean. Some part will store by lake, river, dam, that we mention it as a freshwater.
Hydrology cycle

## Slide 3
Excess rainfall
= observed rainfall – abstractions (interception, depression storage, and infiltration)
Runoff is that portion of precipitation or irrigation on an area that does not infiltrate or evaporate
Streamflow, or discharge, is the volume of water that moves over a designated point over a fixed period of time. The flow of a stream is directly related to the amount of water moving off the watershed into the stream channel.
Direct runoff
= observed streamflow - baseflow
Baseflow is a portion of streamflow that is not directly generated from the excess rainfall during a storm event. In other words, this is the flow that would exist in the stream without the contribution of direct runoff from the rainfall.
Hydrology cycle

## Slide 4
Hydrology cycle
Duration of rainfall excess (D) time from start to finish of rainfall excess
Lag time (L or t p) time from the center of mass of rainfall excess to the peak of the hydrograph
Time of rise (TR)
time from the start of rainfall excess to the peak of the hydrograph
Time of concentration (tc)
time for a wave (of water) propagate from the most distant pt in the watershed to the outlet. One estimate is time from the end of net rainfall to the inflection pt.
Time base (Tb)
total duration of the DRO hydrograph

## Slide 5
Each watershed includes different rainfall stations that spread along the watershed. Since we need to work on one area we consider as a watershed, it is necessary to change the precipitation point to precipitation area.
There are different methods like Thiessen Polygon, Isohyetal Analysis, Arithmetic Mean, Distance Weighting/Gridded, and MAPX.
Mostly use Thiessen Polygon. The individual weights are multiplied by the station observation and the values are summed to obtain the areal average precipitation.
Areal Precipitation

## Slide 6: Areal Precipitation
Isohyetal Analysis which involves drawing estimated lines of equal rainfall over an area based on point measurements. The magnitude and extent of the resultant rainfall areas of coverage are then considered versus the area in question in order to estimate the areal precipitation value.
Rainfall some part of it evaporate, some part recharge groundwater and another part become runoff and discharge of watershed from out let. To estimate direct runoff hydrograph (DRH), we need unit hydrograph.

## Slide 7: Unit hydrograph
Unit hydrograph is a direct runoff hydrograph resulting from one unit (one inch or one cm) of constant intensity uniform rainfall occurring over the entire watershed.
For example, if one mm of excess rainfall produces a direct runoff peak of 100 mm then two mm of excess rainfall with produce a direct runoff of 2 x 100 = 200 mm.

## Slide 8: Unit hydrograph-Example
Compute the total volume of direct runoff.
To do this, add all direct runoff values, and multiply the sum of all the direct runoff flows by the time interval (in seconds) convert cubic feet per second to cubic feet of volume.
After getting the total runoff volume, find the equivalent runoff depth by dividing the runoff volume by the basin area. Note that, the depth thus calculated is equal to the total excess rainfall depth.
We have all data of from a rainfall gauge. Table shows excess rainfall and the consequent direct runoff values are available at 15-minute intervals.

## Slide 9: Unit hydrograph-Example
Calculate Total DRH

## Slide 10: Unit hydrograph-Example
By definition, Unit Hydrograph is a direct runoff hydrograph resulting from the unit depth of effective rainfall. So, the ordinates of required UH can simply be obtained by dividing the ordinates of Direct Runoff Hydrograph by the equivalent depth of total direct runoff.
Next step is to identify its duration.In the dataset above, excess rainfall occurs from 9:30 AM to 12:00 PM, and hence the duration of the derived unit hydrograph is 2.5 hours.

## Slide 11: Unit hydrograph-Example
The conventional graphical representation of the Direct Runoff Hydrograph and the derived Unit Hydrograph ordinates can be obtained by plotting the direct runoff and UH ordinates against time axis in Excel.
The scatter plot hence obtained depicts the direct runoff hydrograph and the derived unit hydrograph of 2.5 hr duration for the given basin.

## Slide 12: Application of Unit Hydrograph to Derive Runoff Hydrograph
Rainfall of P1 inches occurs during a time interval of Δt, the total runoff hydrograph is P1 multiplied by the total unit hydrograph, which is the blue curve (PUH_1) in the figure below.

## Slide 13: Application of Unit Hydrograph to Derive Runoff Hydrograph
Rainfall stops after Δt, this is the direct runoff hydrograph. If the rainfall continues with P2 inches (P2 may or may not be equal to P1) during the next time interval, the total unit hydrograph is
again multiplied by the unit
hydrograph to get the direct
runoff hydrograph from P2
(PUH_2, shown in red).

## Slide 14: Application of Unit Hydrograph to Derive Runoff Hydrograph
Because P2 occurs after Δt, the red curve is delayed or lagged by Δt in the figure. If the rainfall stops after P2, the total runoff hydrograph (green) is the addition of blue curve and
red curve in the figure below.
Rainfall continues with P3, the same procedure is repeated with the P3 component of direct runoff hydrograph delayed by 2*Δt, and added to the red and blue curve to get the total runoff hydrograph.

## Slide 15: Direct runoff and unit hydrograph-Example
A direct runoff hydrograph can be obtained by using the discrete form of convolution integral.
Q=runoff ordinate
P=rainfall pulse
U=unit hydrograph ordinate

## Slide 16: Direct runoff and unit hydrograph-Example
Multiply the entire unit hydrograph (UH) by the first rainfall pulse (P1). Lets call this the PUH_1 hydrograph.
Obtain the PUH_2 hydrograph by multiplying the unit hydrograph by the second rainfall pulse. Delay or lag Q2 by Δt.
Repeat step 2 to obtain PUH_3, PUH_4,..., PUH_M, where M is the total number of rainfall pulses. In this dataset, M = 3 so we can stop after 3. Remember PUH_3 is delayed by additional Δt compared to PUH_2.

## Slide 17: Direct runoff and unit hydrograph-Example
Sum all the PUH columns (PUH_1 + PUH_2 + ....+ PUH_M) to get the direct runoff hydrograph. The total number of direct runoff ordinates (N) must be equal to U + M – 1. Where U is the total number of unit hydrograph ordinates.
Yellow cells represent the unit hydrograph
Green cells represent the precipitation
Purple cells represent PUH
Blue cells represent the total runoff hydrograph

## Slide 18: UNIT HYDROGRAPHS-Example
Obtain a Unit Hydrograph for a basin of 282.6 of area using the rainfall and streamflow date
Use the horizontal straight-line method to separate baseflow.
Separate the baseflow from the observed streamflow hydrograph in order to obtain the Direct Runoff Hydrograph (DRH).
For this example, use the horizontal line method to separate the baseflow. From observation of the hydrograph data, the streamflow at the start of the rising limb of the hydrograph is 150 . Thus, use 150 as the baseflow.
Compute the volume of Direct Runoff. This volume must be equal to the volume of the Effective Rainfall Hyetograph (ERH).
VDRH = (200+650+1050+750+600+400+200+75) m3/s (3600) s = 14'130,000 m3
Time (h) | Observed Hydrograph (m3/s)
0 | 160
1 | 150
2 | 350
3 | 800
4 | 1200
5 | 900
6 | 750
7 | 550
8 | 350
9 | 225
10 | 150
11 | 140
Time (h) | Gross Precipitation (GRH) (cm/h)
0 - 1 | 0.25
1 - 2 | 2.75
2 - 3 | 2.75
3 - 4 | 0.25

## Slide 19: UNIT HYDROGRAPHS-Example
Express VDRH in equivalent units of depth:
VDRH in equivalent units of depth = VDRH/Abasin
= 14'130,000 m3/(282600000 m2) = 0.05 m = 5 cm
Obtain a Unit Hydrograph by normalizing the DRH. Normalizing implies dividing the ordinates of the DRH by the VDRH in equivalent units of depth.
Obtain a Unit Hydrograph for a basin of 282.6 of area using the rainfall and streamflow date

## Slide 20: UNIT HYDROGRAPHS-Example
Determine the duration D of the ERH associated with the UH obtained in 4. In order to do this:
  Determine the volume of losses, VLosses which is equal to the difference between the volume of gross rainfall, VGRH, and the volume of the direct runoff hydrograph, VDRH.
  Compute the f-index equal to the ratio of the volume of losses to the rainfall duration, tr. Thus
  f-index = VLosses/tr = 1 cm / 4 h = 0.25 cm/h
  Determine the ERH by subtracting the infiltration (e.g., f-index) from the GRH
VLosses = VGRH - VDRH
= (0.25 + 2.75 + 2.75 +0.25) cm/h 1 h - 5 cm = 1 cm
Obtain a Unit Hydrograph for a basin of 282.6 of area using the rainfall and streamflow date

## Slide 21: UNIT HYDROGRAPHS-Example
As observed in the table, the duration of the effective rainfall hyetograph is 2 hours. Thus, D = 2 hours, and the Unit Hydrograph obtained above is a 2-hour Unit Hydrograph. Therefore, it can be used to predict runoff from precipitation events whose effective rainfall hyetographs can be represented as a sequence of uniform intensity (rectangular) pulses each of duration D. This is accomplished by using the principles of superposition and proportionality, encoded in the discrete convolution equation:
Qn = nth ordinate of the DRH
Pm = volume of the mth rainfall pulse expressed in units of equivalent depth (e.g., cm or in)
Un-m+1 = the (n-m+1)th ordinate of the UH
expressed in units of m3/s/cm.
Obtain a Unit Hydrograph for a basin of 282.6 of area using the rainfall and streamflow date

## Slide 22: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Time (h) | Effective Precipitation (ERH) (cm/h)
0 - 1 | 1.0
1 - 2 | 1.0
2 - 3 | 1.5
3 - 4 | 1.5
4 - 5 | 0.75
5 - 6 | 0.75
6 - 7 | 0.25
7 - 8 | 0.25
Use the same value of baseflow as for Problem 1.
As observed in the table, the ERH can be decomposed into a sequence of rectangular pulses, each of 2 hours duration. Thus, we can use the 2-hour UH obtained in Problem 1.
Time (h) | Pm (cm)
0 - 2 | 2.0
2 - 4 | 3.0
4 - 6 | 1.5
6 - 8 | 0.5
Determine the volume of each ERH pulse, Pm, expressed in units of equivalent depth.

## Slide 23: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Use superposition and proportionality principles
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Time (h) | UH (m3/s/cm) | P1*UH (m3/s) | P2*UH (m3/s) | P3*UH (m3/s) | P4*UH (m3/s) | DRH (m3/s) | Total (m3/s)
1 | 0.00 | 0.00 |  |  |  | 0.00 | 150.00
2 | 40.00 | 80.00 |  |  |  | 80.00 | 230.00
3 | 130.00 | 260.00 | 0.00 |  |  | 260.00 | 410.00
4 | 210.00 | 420.00 | 120.00 |  |  | 540.00 | 690.00
5 | 150.00 | 300.00 | 390.00 | 0.00 |  | 690.00 | 840.00
6 | 120.00 | 240.00 | 630.00 | 60.00 |  | 930.00 | 1080.00
7 | 80.00 | 160.00 | 450.00 | 195.00 | 0.00 | 805.00 | 955.00
8 | 40.00 | 80.00 | 360.00 | 315.00 | 20.00 | 775.00 | 925.00
9 | 15.00 | 30.00 | 240.00 | 225.00 | 65.00 | 560.00 | 710.00
10 | 0.00 | 0.00 | 120.00 | 180.00 | 105.00 | 405.00 | 555.00
11 |  |  | 45.00 | 120.00 | 75.00 | 240.00 | 390.00
12 |  |  | 0.00 | 60.00 | 60.00 | 120.00 | 270.00
13 |  |  |  | 22.50 | 40.00 | 62.50 | 212.50
14 |  |  |  | 0.00 | 20.00 | 20.00 | 170.00
15 |  |  |  |  | 7.50 | 7.50 | 157.50
16 |  |  |  |  | 0.00 | 0.00 | 150.00
Columns 2 – 5：
  Apply the proportionality principle to scale the UH by the actual volume of the corresponding rectangular pulse, Pm. Observe that the resulting hydrographs are lagged so that their origins coincide with the time of occurrence of the corresponding rainfall pulse.
Column 6：
  Apply the superposition principle to obtain the DRH by summing up Columns 2 - 5.
Column 7：
  Add back the baseflow in order to obtain the Total Streamflow Hydrograph.

## Slide 24: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Use superposition and proportionality principles

## Slide 25: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Use the 1-h Unit Hydrograph tabulated below to predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall is also tabulated below. Use the same value of baseflow as for Problem 1. Obtain the solution using the S-Hydrograph method.
Time (h) | 1-H Unit Hydrograph (m3/s/cm)
1 | 0.00
2 | 40.00
3 | 130.00
4 | 210.00
5 | 150.00
6 | 120.00
7 | 80.00
8 | 40.00
9 | 15.00
10 | 0.00
Time (h) | Effective Precipitation (ERH) (cm/h)
0 - 3 | 1.0
3 - 6 | 2.0
6 - 9 | 1.5

## Slide 26: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Observe that the S-hydrograph is obtained in 2 different ways
  In tabular form as the superposition of an infinite sequence of 1-h UH's each lagged by 1-h.
Time (h) | UH | UH(t-1) | UH(t-2) | UH(t-3) | UH(t-4) | UH(t-5) | UH(t-6) | UH(t-7) | UH(t-8) | UH(t-9) | S-Hydr.
單位 | (m3/s/cm) |  |  |  |  |  |  |  |  |  | 
1 | 0 |  |  |  |  |  |  |  |  |  | 0
2 | 40 | 0 |  |  |  |  |  |  |  |  | 40
3 | 130 | 40 | 0 |  |  |  |  |  |  |  | 170
4 | 210 | 130 | 40 | 0 |  |  |  |  |  |  | 380
5 | 150 | 210 | 130 | 40 | 0 |  |  |  |  |  | 530
6 | 120 | 150 | 210 | 130 | 40 | 0 |  |  |  |  | 650
7 | 80 | 120 | 150 | 210 | 130 | 40 | 0 |  |  |  | 730
8 | 40 | 80 | 120 | 150 | 210 | 130 | 40 | 0 |  |  | 770
9 | 15 | 40 | 80 | 120 | 150 | 210 | 130 | 40 | 0 |  | 785
10 | 0 | 15 | 40 | 80 | 120 | 150 | 210 | 130 | 40 | 0 | 785
11 |  | 0 | 15 | 40 | 80 | 120 | 150 | 210 | 130 | 40 | 785
12 |  |  | 0 | 15 | 40 | 80 | 120 | 150 | 210 | 130 | 785
13 |  |  |  | 0 | 15 | 40 | 80 | 120 | 150 | 210 | 785
14 |  |  |  |  | 0 | 15 | 40 | 80 | 120 | 150 | 785
15 |  |  |  |  |  | 0 | 15 | 40 | 80 | 120 | 785
16 |  |  |  |  |  |  | 0 | 15 | 40 | 80 | 785
17 |  |  |  |  |  |  |  | 0 | 15 | 40 | 785
18 |  |  |  |  |  |  |  |  | 0 | 15 | 785
19 |  |  |  |  |  |  |  |  |  | 0 | 785

## Slide 27: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Observe that the S-hydrograph is obtained in 2 different ways
  The cumulative volume of UH per unit time.
 | 1 | 2 | 3 | 4 | 5
Time (h) | 1-h UH (m3/s/cm) | S-Hyd (m3/s/cm) | Lagged S-Hyd (m3/s/cm) | S1-S2 (m3/s/cm) | D'-UH (m3/s/cm)
1 | 0 | 0 |  | 0 | 0
2 | 40 | 40 |  | 40 | 13.33333
3 | 130 | 170 |  | 170 | 56.66667
4 | 210 | 380 | 0 | 380 | 126.6667
5 | 150 | 530 | 40 | 490 | 163.3333
6 | 120 | 650 | 170 | 480 | 160
7 | 80 | 730 | 380 | 350 | 116.6667
8 | 40 | 770 | 530 | 240 | 80
9 | 15 | 785 | 650 | 135 | 45
10 | 0 | 785 | 730 | 55 | 18.33333
11 |  | 785 | 770 | 15 | 5
12 |  | 785 | 785 | 0 | 0
13 |  | 785 | 785 | 0 | 0
14 |  | 785 | 785 | 0 | 0

## Slide 28: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Determine the volume of each ERH pulse, Pm, expressed in units of equivalent depth.
Time (h) | Pm (cm)
0 - 2 | 2.0
2 - 4 | 3.0
4 - 6 | 1.5
6 - 8 | 0.5

## Slide 29: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Use superposition and proportionality principles
Columns 2 – 4：
  Apply the proportionality principle to scale the UH by the actual volume of the corresponding rectangular pulse, Pm. Observe that the resulting hydrographs are lagged so that their origins coincide with the time of occurrence of the corresponding rainfall pulse.
Column 5：
  Apply the superposition principle to obtain the DRH by summing up Columns 2 - 4.
Column 6：
  Add back the baseflow in order to obtain the Total Streamflow Hydrograph.
 | 1 | 2 | 3 | 4 | 5 | 6
Time(h) | UH (m3/s/cm) | P1*UH (m3/s) | P2*UH (m3/s) | P3*UH (m3/s) | DRH (m3/s) | Total (m3/s)
1 | 0 | 0 |  |  | 0 | 150
2 | 13.33333 | 40 |  |  | 40 | 190
3 | 56.66667 | 170 |  |  | 170 | 320
4 | 126.6667 | 380 | 0 |  | 380 | 530
5 | 163.3333 | 490 | 80 |  | 570 | 720
6 | 160 | 480 | 340 |  | 820 | 970
7 | 116.6667 | 350 | 760 | 0 | 1110 | 1260
8 | 80 | 240 | 980 | 60 | 1280 | 1430
9 | 45 | 135 | 960 | 255 | 1350 | 1500
10 | 18.33333 | 55 | 700 | 570 | 1325 | 1475
11 | 5 | 15 | 480 | 735 | 1230 | 1380
12 | 0 | 0 | 270 | 720 | 990 | 1140
13 |  |  | 110 | 525 | 635 | 785
14 |  |  | 30 | 360 | 390 | 540
15 |  |  | 0 | 202.5 | 202.5 | 352.5
16 |  |  |  | 82.5 | 82.5 | 232.5
17 |  |  |  | 22.5 | 22.5 | 172.5
18 |  |  |  | 0 | 0 | 150

## Slide 30: UNIT HYDROGRAPHS-Example
Predict the total streamflow hydrograph that would be observed as a result of a storm whose effective rainfall.
Use superposition and proportionality principles
 | 1 | 2 | 3 | 4 | 5 | 6
Time(h) | UH (m3/s/cm) | P1*UH (m3/s) | P2*UH (m3/s) | P3*UH (m3/s) | DRH (m3/s) | Total (m3/s)
1 | 0 | 0 |  |  | 0 | 150
2 | 13.33333 | 40 |  |  | 40 | 190
3 | 56.66667 | 170 |  |  | 170 | 320
4 | 126.6667 | 380 | 0 |  | 380 | 530
5 | 163.3333 | 490 | 80 |  | 570 | 720
6 | 160 | 480 | 340 |  | 820 | 970
7 | 116.6667 | 350 | 760 | 0 | 1110 | 1260
8 | 80 | 240 | 980 | 60 | 1280 | 1430
9 | 45 | 135 | 960 | 255 | 1350 | 1500
10 | 18.33333 | 55 | 700 | 570 | 1325 | 1475
11 | 5 | 15 | 480 | 735 | 1230 | 1380
12 | 0 | 0 | 270 | 720 | 990 | 1140
13 |  |  | 110 | 525 | 635 | 785
14 |  |  | 30 | 360 | 390 | 540
15 |  |  | 0 | 202.5 | 202.5 | 352.5
16 |  |  |  | 82.5 | 82.5 | 232.5
17 |  |  |  | 22.5 | 22.5 | 172.5
18 |  |  |  | 0 | 0 | 150

## Slide 31: GIS Create Watershed

## Slide 33
坡度Slope
要分析的DEM

## Slide 35
坡向Aspect
要分析的DEM

## Slide 37
無窪地DEM處理
＊將DEM填滿窪地

## Slide 38
水流方向
Flow Direction
要分析的網格

## Slide 40
窪地分析
流向網格

## Slide 42
窪地集水區分析
流向網格
網格或圖徵匯流點資料

## Slide 43
＊黑色區塊=流向窪地的集水區

## Slide 44
窪地集水區最低高程
原始DEM
網格或圖徵匯流點資料
MINIMUM

## Slide 46
出水口最小計算
原始DEM
區域網格

## Slide 48
窪地深度
出水口高程-集水區高程Min

## Slide 50
窪地填充
原始DEM

## Slide 52
無窪地DEM流向
要分析的網格
儲存位置

## Slide 53
＊符合D8流向編碼設定

## Slide 54
匯流累積量及水流長度分析

## Slide 55
匯流累積量
流向網格
INTEGER=整數

## Slide 58
水流長度分析
流向網格
順流=DOWNTREAM
溯源=UPSTREAM
UPSTREAM以作為上游集流時間分析參考

## Slide 60
河川網絡分析

## Slide 61
河網萃取
條件網格
1
”Value” > 1000

## Slide 63
河網網格轉線段圖徵
河網網格
流向網格

## Slide 65
畫出節點
圖徵
START=匯出河段起始點

## Slide 67
河網連結分段
河網網格
流向網格

## Slide 69
河段分級
河網網格
流向網格
Strahler分級
Strahler 分級是將所有河段中沒有支流河段分為第1 級，兩個 1 級河段匯流成的河段為第 2 級，如此下去分別為第 3 級，第 4 級， 一直到河網出水口。在這種分級中，僅當同級別的兩條河段匯流成一條河段 時，該弧段級別才會增加，對於那些低級弧段匯入高級弧段的情況，高級弧段的級別不會改變，這也是比較常用的一種河網分級方法。
Shreve分級
Shreve 分級，其第 1 級河網的定義與 Strahler 分級相同，而由兩條河段匯流而成的河段會做級別的加總，當一條3級河段和一條4級河段匯流而成的新的河段的級別就是7。以此分級到最後出水口的位置時，其河網的級別數剛好是該 河網中所有的 1 級河段的個數。

## Slide 71
流域分析

## Slide 72
集水區分割
儲存位置
流向網格
網格或匯流點資料

## Slide 75: PIX4D

## Slide 76: Project Setting
Create New Prolect

## Slide 77: Project Setting
1
2

## Slide 78
1
2 (Select Images)
3 (Open)
Project Setting
Select Images

## Slide 79: Project Setting
Select Images

## Slide 80: Project Setting

## Slide 81: Project Setting
Select Output Coordinate System

## Slide 82: Project Setting
1
2
Template

## Slide 84: GCP Manager

## Slide 85: GCP Manager
Change GCP Coordinate System
2
3
1

## Slide 86: GCP Manager
Input GCP Points
1
2

## Slide 87
Basic Editor
1
2
3
Click
GCP Manager

## Slide 88: GCP Manager
GSD
GSD

## Slide 89: Processing Options
OR

## Slide 90: Running

## Slide 91: Result

## Slide 92: Output
Report | ..\<Project_Name>\1_initial\report
3D Mesh | ..\<Project_Name>\2_densification\3d_mesh
DSM | ..\<Project_Name>\3_dsm_ortho\1_dsm
Mosaic | ..\<Project_Name>\3_dsm_ortho\2_mosaic
3D Mesh
Report

## Slide 93: Output
Report | ..\<Project_Name>\1_initial\report
3D Mesh | ..\<Project_Name>\2_densification\3d_mesh
DSM | ..\<Project_Name>\3_dsm_ortho\1_dsm
Mosaic | ..\<Project_Name>\3_dsm_ortho\2_mosaic
Mosaic
DSM

## Slide 94
Soil and Water Conservation TAIWAN
Thank You